## Slide 1: Predicting Cardiac Output from Arterial Blood Pressure
Team 9
Sejal Ghate
Zixu Han
Yongzhi Sun

## Slide 2
#s00214
#s05114
#s00020
ABP and derived features from three subjects for 20 peaks

## Slide 3
Continuous: Estimated CO
Calibration (C2): Calibration_factor=COtd(1)/Uncalibrated_CO
Stem: COtd measurements at different times
Continuous PP, MAP and HR are derived from computed feature matrix
Stem plot: PPs, MAPs, HRs that are measured at the same time as COtd measurements
Estimated CO from Liijestrandand algorithm - #s00020
Liljestrand estimation: Estimator 5

## Slide 4
Repeat CO estimation with three other algorithms
Systolic area with Kouchoukos correction
Herd
Calibration: the same as the one used in Liljestrand algorithm (C2)
Parlikar
Calibration: least-square-error

## Slide 5
Estimated CO - #s00020 for the first 12 hours
Liljestrand
Systolic area with Kouchoukos correction
Herd
Parlikar with filt_order = 15

## Slide 6: CO Calibration using Parlikar’s method:
Sliding Window approach:
  Window size 21
  Filtering used: filter order 15
  τ calculated for each index within the window
  Least squares solution used to assign the value obtained from the β equation
  This value is assigned to center most index in the window
  Window slides by one index
  To account for indexes which cannot be mid-points for any window (left and right extreme indexes), Values interpolated to nearest non-zero value (i.e, first non-zero and last non-zero values respectively)
Calibration: C2 and least square ‘ϒ’ calibration

## Slide 7
Estimated CO with two other subjects
Liljestrand
Systolic area with Kouchoukos correction
Herd
#s00214
#s05114
Parlikar

## Slide 8
Total peripheral resistance calculated after Parlikar estimation
Formula used for TPR:
Feature matrix extracted from the modified estimated_co code
Calculation performed on variables of this feature matrix
Appropriate conversion applied for TPR units to mmHg/(mL/s)

## Slide 9
Bland-Altman Analysis for algorithm comparison based on each paired COtd-estimated_CO
Error Distributions of each paired CO-from-ABP and COtd for each algorithm
X axis-Mean value: (Estimated CO + Cotd)/2
Y axis-Difference: Estimated CO – Cotd
Mean Difference: Sum of Y /no.Cotd
95% limits of agreement: Mean Difference±1.96SD
95% limits of agreement

## Slide 10
Liljestrand
Systolic area w/ Kouchoukos correction
Herd
Parlikar
#s00020
#s00214
#s05114
Liljestrand

## Slide 11: Difficulties and interesting observations associated with project:
Sample selection: Unlike sample 20, the waveforms of many samples are chaotic and do not show waveforms similar to those expected, feature extraction might not always be the most accurate due to presence of ectopic beats and outliers in the signal.
Our solution: Manually screen the data and find a better waveform for analysis
There are questions about the selection of V2 and V3 algorithms
Our solution: Choose the simpler V3 algorithm among the two methods
Extreme values appear in the Parlikar estimated COs
Our solution: Increase the filter order to 15 in estimate_co_v3 function.
What’s interesting? : Higher frequency waveform data! Need not always be clean, is very noisy, and due to different instruments used needs a lot of ‘reverse engineering’ to find similarities in different data frames.

## Slide 12: Individual contribution:
Sejal Ghate : Question 1,3,5,6
01
Zixu Han : Question:3,4,5
02
Yongzhi Sun: Question: 1,2,3
03